## Slide 1: Traffic Signal Detection System
Team Members:
Vrushabh Desai, Rishi Madduri, Kavit Shah
RBE 549- COMPUTER VISION FINAL PROJECT PRESENTATION

## Slide 2: Objectives
Minimum Goals
  To implement object detection algorithm to detect traffic lights.
  To implement classifier to detect the signals accurately.
Improved Goals
  To analyze results using different object recognition algorithms.
  To implement YOLO Neural Networks

## Slide 3: Introduction
Key features of project
  Use of Classical Computer Vision Methods:
SIFT and SURF
Top Hat Filter
Hough
YOLO
  Neural Networks for Object Detection
Statement of Purpose
  To avoid accidents through detecting traffic signals accurately.
  To implement robust algorithm to detect signals at day, night, while in motion, etc...

## Slide 4: SIFT and SURF

## Slide 5: SIFT and SURF

## Slide 6: SIFT and SURF

## Slide 7: Top Hat Filter:
A Mathematical Morphology Operation
Can Be Used to Extract Details from Image
Two Types of Top Hat Filters:
  White Top Hat
    Difference between an Input Image and its Opening By a Structural Element
  Black Top Hat
    Difference between Closing by a Structural Element and Input Image
.

## Slide 8: Top Hat Filter Implementation
Read Image
Convert from RGB to Grayscale
Select a structuring element
Opening the image followed by subtraction of the result from the original image
Applying Gaussian Filter to reduce false positives
Applying SURF Feature Detector to detect Key Points
Plotting the Key Points

## Slide 9: Test-1

## Slide 11: Test 2

## Slide 13: Test 3

## Slide 15: Hough Implementation
  Initial steps:
Import image and convert it into HSV colour space
Set colour ranges for red, green and yellow lights.
  Hough implementation:
Mask the HSV colour spaces with colour ranges initialized.
Implement Hough to detect circles and get its parameters.
Implement opening for reducing noise.
Draw the circle on detected hough circles.

## Slide 16: Case-1: Hough on Red lights
  Masking:
It recalculates each pixel's value in an image according to a mask matrix.
By applying a mask M on an image I, the pixels of I whose corresponding pixel in M are true are copied into a new image. The rest of the pixels in the new image are set to 0.
From a mathematical point of view we make a weighted average, with our specified values.

## Slide 17: Masked image and result after opening
Before opening
After opening

## Slide 18: Case-2: Hough on green lights

## Slide 19: Case-2: Results
Before opening
After opening

## Slide 20: Case-3: Drawback with Hough

## Slide 21: Case-3: Results
Before opening
After opening

## Slide 22: YOLOv3:
Used for real time object detection
It has 106 CNN layer which is used to detect object features in the frame.
Pre-trained model can detect up to 80 different objects (eg: Traffic signal, car, chair, etc.)

## Slide 23: Bounding Box
Network creates a bounding box around the features that could probably be an object.
The width of the box defines the probability or confidence of object belonging to a particular class.
We modified the model to detect traffic light.

## Slide 24: Yolov3 detection on a single Image

## Slide 25: Recognition using Thresholding
Red mask
count: 0
Yellow mask
count: 0
Green mask
count: 63
Red mask
count: 0
Yellow mask
count: 0
Green mask
count: 29
Red mask
count: 0
Yellow mask
count: 0
Green mask
count: 43
Declare GO
Declare GO
Declare GO

## Slide 26: YoloV3 - Real Time Detection

## Slide 27: YoloV3 - Real Time Detection

## Slide 28: Detection in different lighting conditions

## Slide 29: Results and Conclusion
  Results:
Successfully implemented different object recognition algorithms.
Implemented YOLO algorithm using pre-trained model to detect traffic signal accurately.
Achieved real-time object recognition
Implemented robust algorithm to detect signals at day, night, while in motion, etc...
  Conclusion:
SIFT & SURF: not invariant to change in perspective.
Top Hat filter with SURF: not invariant to change in perspective
Hough Transform: Does not distinguish between the object and the background due to predefined HSV colour space.
Yolov3: Robustly detects traffic signals under different perspectives and lighting conditions

## Slide 30: References
[1] Data Set: http://computing.wpi.edu/dataset.html
[2] https://www.cyberailab.com/home/a-closer-look-at-yolov3
[3] https://pjreddie.com/darknet/yolo/
[4] Müller, Julian and Klaus C. J. Dietmayer. “Detecting Traffic Lights by Single Shot Detection.” 2018 21st International Conference on Intelligent Transportation Systems (ITSC) (2018): 266-273.
[5] R. de Charette and F. Nashashibi, "Real time visual traffic lights recognition based on Spot Light Detection and adaptive traffic lights templates," 2009 IEEE Intelligent Vehicles Symposium, Xi'an, 2009, pp. 358-363.
doi: 10.1109/IVS.2009.5164304
[6] https://arxiv.org/abs/1506.02640
[7] R. de Charette and F. Nashashibi, "Traffic light recognition using image processing compared to learning processes," 2009 IEEE/RSJ International Conference on Intelligent Robots and Systems, St. Louis, MO, 2009, pp. 333-338.
doi: 10.1109/IROS.2009.5353941

## Slide 31
THANK YOU!